## Slide 1: Striclty for educational purposes
Final project in M.Sc. Course for teachers, in the framework of the Caesarea –Rothschild program of the Feinberg Grad School of the Weizmann inst. of Science.
Note that ppt may contain copy-righted material and as such any use that can violate such rights will require permission from the © holders.

## Slide 2: Better Place Unrealized Dream
By Nathalie Baskin
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 3: Table of Contents
Introduction
Technology
Calculations
Discussion
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 4: Introduction
Cars
Car’s Role: travel, quality of life –the private car has
huge impact on industrial and farm.
1. Not familiar with this subject at all.
2. Israel started to construct very expensive infrastructure for electrical transport, but the electrical private cars failed.
Why did I choose this subject?
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 5
Fuel is matter that releases a lot of energy when burned. Ordinary cars use fuel that originally comes from oil.
The reaction is irreversible oxidation.
Byproducts:
CO, Hydrocarbons, Nitrogen oxides NOx, Sulfur oxides, smoke.
Fuel originally from oil
We breath the pollution in relatively high concentrations.
What’s the Problem?
Source of Oil - finite
Technology
Ordinary Cars
Amount of high CO2 can cause global warming of the Earth.
C8H18+12.5O28CO2+9H2O
Environmental Noise near the residence
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 6
Technology
The result:
1. No need to use Oil
2. No pollution during use
3. No noise on the roads
Electrical Car
Redox reaction:
The flow of electrons between the electrodes and their ∆{potential (=voltage)} causes electric current, which drives an electrical engine.
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 7: Technology
Electrical Car
Electrochemical cell – Cell based on redox reversible reaction.
In a Battery, flow of electrons from cathode to anode, generates electricity.
To charge a Battery– flow of electrons from anode to cathode.
http://www.youtube.com/watch?v=J1ljxodF9_g
Requirements of car battery:
1.Low mass
2.High voltage
Electric battery
http://www.fccj.us/chm2046/SampleTest/46M14eAnswer.htm
Best cathode will be made of Li (solid with lowest molar mass : 7 gm / mol and highest voltage 3.04 V).
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 8: Battery's Energy Density
http://funginstitute.berkeley.edu/sites/default/files/The%20Electric%20Vehicle%20Battery%20Landscape%20-%20Opportunities%20and%20Challenges.pdf
Energy density
Li ion batteries can generate relatively high voltage, with currents comparable to other batteries  very high energy density.
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 9
http://www.mpoweruk.com/chemistries.htm
Discharge mechanism
Charge mechanism
Flow of electrons
http://www.youtube.com/watch?v=2PjyJhe7Q1g
engine
מנוע
http://electronics.howstuffworks.com/everyday-tech/lithium-ion-battery1.htm
How do Li+ (Li ion) Batteries Work?
Animations of the work of Li ion battery.
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 10: Car Batteries – Base Data
http://www-scf.usc.edu/~rzhao/LFP_study.pdf
Is there a preferred battery?
Better Place used LiFePO4 batteries (came with its Renault Fluence Z.E. cars)
Tesla cars use LiCoO2 batteries
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 11: Lithium ion Batteries in an Electric Car.
Now we will focus on battery itself
Batteries for Electric Cars – BCG research
Success of the electric car dependent of:

## Slide 12: Content of Lithium-Ion Battery LCO LiCoO2
http://www.teslamotors.com/it_IT/forum/forums/technical-battery-discussion
Cell voltage: 3.8 V
ECell = ECathode − EAnode
Positive Electrode
Negative Electrode
The Chemical reaction that occurs in the cell:
No of Cells: 6831
11 modules
Each module consists of 9 bricks (99 cells in series)
Total of about 69 bricks in parallel
Each cell mass is 44.5 gm
Over-all voltage of the battery 375 V
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 13
http://www.intechopen.com/books/metal-ceramic-and-polymeric-composites-for-various-uses/composite-cathode-material-for-li-ion-batteries-based-on-lifepo4-system-
Standard Battery: 60 kWh – for range of 335 km costs 10,000 $
Improved Battery: 85 kWh – for range of 426 km costs 12,000 $
What is inside the LiCoO2 Li+ Battery ?
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 14: Chemistry of the Battery
ΔG°cell = −nFE°cell
Cell Energy
Over-charge
Over-discharge
The Cobalt electrode reaction is only reversible for n < 0.5
http://en.wikipedia.org/wiki/Lithium-ion_battery
Limitations of battery: over-load or full discharge Irreversible reaction  spoils the battery.
Co(III)  Co(IV) during charge
Co(IV)  Co(III) during discharge
Positive Electrode
Negative Electrode
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 15: Content of Lithium-Ion Battery LFP LiFePO4
No of Cells: 192
3 stacks in which 16 modules
Each module consists of 4 cells
Capacity 65 Ah
Battery’s Voltage 398 V
http://www.renault.com/en/innovation/gamme-mecanique/pages/batterie-moteur-electrique.aspx
http://www.renault.com/en/innovation/vehicule-electrique/pages/electro-techno.aspx
Price - 45,000 $
Renault Fluence ZE Technical Specifications
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 16: Lithium ion battery LiFePO4
http://www.pedaily.cn/Item.aspx?id=194151
http://www.intechopen.com/books/metal-ceramic-and-polymeric-composites-for-various-uses/composite-cathode-material-for-li-ion-batteries-based-on-lifepo4-system-
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 17: Chemistry of Battery
Cell voltage : 3.4 V
ΔG°cell = −nFE°cell
Cell Energy
http://www.intechopen.com/books/metal-ceramic-and-polymeric-composites-for-various-uses/composite-cathode-material-for-li-ion-batteries-based-on-lifepo4-system-
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 18: Lithium-ion Batteries in an Electric Car. Comparison
Battery LiCoO2
Battery LiFePO4
Recharging 420 times
Cobalt is toxic
Cathode of battery is very expensive $ 35.32 /kg
Overheating destroys battery
Can explode without known cause
Cathode of battery relatively inexpensive
$ 4.45 /kg
Highest energy density
Highest power density
http://funginstitute.berkeley.edu/sites/default/files/The%20Electric%20Vehicle%20Battery%20Landscape%20-%20Opportunities%20and%20Challenges.pdf
Efficiency 80%
Chart: 
| energy dencity | power density | safety | cycle life 80% | production price | Performance
LFP | 2 | 3 | 4 | 4 | 3 | 3
LCO | 4 | 3 | 2 | 3 | 3 | 3
Recharging > 7000 times
Very safe against explosion; heat resistant
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 19: Lithium ion batteries electric car. Comparison
Batteries for Electric Cars – BCG research
We talked
about those
and continue
with these
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 20: Cell cost break-down of the major components
The Electric Vehicle Battery Landscape: Opportunities and Challenges. Center for Entrepreneurship & Technology (CET). Technical Brief. Number: 2009.9.v.1.1.
Comparison of batteries containing 18650 cells with similar performance
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 21: Lithium ion batteries in an electric car
LiFePO4 Battery’s Density
LiCoO2 Battery’s Density
Gasoline -6
Materials for Energy – Ginley and Cahen
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 22
From the data can be seen that the differences between the two types of batteries are not very significant.
Materials for Energy – Ginley and Cahen
Energy and Power Densities of Batteries relative to those of Fuel
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 23: Transportation Energy Data 2012
1.8 tonne of fuel /vehicle – year
0.7 kg / liter - density of gasoline
0.85 kg / liter - diesel density
~2,500 liters of fuel /vehicle - year
Gasoline ~2.5 . 106 tonne /year
Diesel oil ~2.5 . 106 tonne /year
Overall ~5 .106 tonne of fuel per year
Approximately -2.75 . 106 motorized vehicles in Israel
Assume average fuel consumption (averaged city & intercity roads) –10 km/l and average distance driven/year 24,500 km.
Fuel consumption data - Ministry of National Infrastructures, Energy and Water, 2012
Motorized vehicles, by type - Central Bureau of Statistics
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 24: Average Israel ~24,000 km / year
Annual savings in terms of Gasoline / car-year: 16,000 NIS
More practical:
Average includes all vehicles;
Here are calculation for private cars, that drive 16000 km/year
Overall - 5 . 106 tons of fuel / year
6.5 .109 liters of fuel /year
which cost ~5.1010 NIS/year
The savings is 7 times the current price!
7 . 109 NIS / yr
or 7 . 105 tons of fuel / yr !
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.
Notes: 6.5 .106 liters of fuel /year
does not make sense
so, I changed it to 10**9
Check also the following
7 billion shekels per year or 700 thousand tons of fuel per year instead of 5000 tons!

## Slide 25: Private car’s total fuel cost/year
Average distance Car a year – 16,000 km
Price per liter of gasoline – 7.70 NIS
Price per liter of diesel fuel – 6.13 NIS
(2012)
1,600 liters of fuel
Fuel price about 12,320 NIS
Assuming an average fuel consumption (both city and intercity roads) - 10 km / liter
Power consumption Manufacturer data:
0.175 kWh/km
Driving a Tesla car 16,000 km
requires 2,800 kWh.
Equivalent charging cost at night 1036 NIS
Standard Car
Electric Car
Price per kWh at night – 0.3711 NIS
Price per kWh during peak hours – 1.2853 NIS
Tesla S
Renault Fluence Z.E.
Power consumption Manufacturer data:
0.275 kWh/km
Driving a Renault car 16,000 km
requires 4,400 kWh.
Equivalent charging cost at night 1628 NIS
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.
Notes: How did we get from 24,000 km/yr to 16,000 km/yr

## Slide 26
Chart: Fuel Prices / charge for the year
| NIS/16000 km | NIS/24000 km
Tesla S | 1039 | 1559
Renault Fluence ZE | 1632 | 2449
Premium Sedan | 12320 | 18480
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 27
Chart: Price of fuel or charging /year @ highest electricity prices
| NIS/16000 km | NIS/24000 km
Tesla S | 3598 | 5397
Renault Fluence ZE | 5654 | 8481
Premium Sedan | 12320 | 18480
Price per kWh during peak hours – 1.2853 NIS
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 28: Better Place: Financial Loss
http://www.themarker.com/dynamo/1.1865169
http://www.themarker.com/dynamo/1.2038520
05.06.2013
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 29: So how Better Place went bankrupt?
Misguided economic management
Battery is very expensive
Infrastructure and ease of use
Technology fails
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 30
Chart: 
| km | price (NIS)
Tesla S | 330 | 240
Renault Fluence ZE | 160 | 123
standard car | 420 | 120
Price of the car vs. distance at full tank (full Charge)
Excluding the price of the battery; car purchase requires subscription to battery and service.
Price includes battery, domestic charging stand + 8 year service.
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 31: Infrastructure - a standard car
Customer friendly gas stations
 | No. of fuel stations in the country | place | Fueling time | No. of cars at a gas station
Gasoline and diesel | 2040 | Public space | 5 minutes | 1353 cars in one gas station
Approximately -2.761 million vehicles in Israel
Type of station | No. of stations in the country | Place | Charging time (fastest) |  | No. of car charging stations
 |  |  | Better Place | Tesla | 
Charging | 1850 | Public spaces and individual stations | Fast: 30 minutes Standard: 6-8 hours | 66 sec | 2 docking stations for each vehicle
Swap | 38 | Public spaces | 5 minutes | 90 sec | 
Only 900 cars in Israel
Private parking is required for any electric car owner
Infrastructure - electric cars
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 32: Electric Cars
http://www.globes.co.il/news/article.aspx?did=1000723370
09/02/2012
38 stations for quick replacement of batteries - Convenient and quick method.
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 33: Weight and price
http://blog.truecar.com/2013/01/17/spotlight-on-technology-how-safe-are-lithium-ion-battery-packs/
http://www.caranddriver.com/reviews/2013-tesla-model-s-test-review
Type of battery | Price considering battery life time (NIS\km) | Car battery weight | Volume
LiFePO4 battery(better place) | 0.23 km/nis (long life time (validity)) Battery of 303 kg | 280 kg | 218 liters in trunk
LiCoO2 battery (Tesla) | 0.29km/nis (fast life time (validity)) Battery of 261 kg | 600 kg | Automobile belly
http://www.cartube.co.il/road-test/renault-road-test/%D7%A8%D7%A0%D7%95-%D7%A4%D7%9C%D7%95%D7%90%D7%A0%D7%A1-Z-E-%D7%9E%D7%91%D7%97%D7%9F-%D7%93%D7%A8%D7%9B%D7%99%D7%9D-%E2%80%93-%D7%A4%D7%9C%D7%95%D7%90%D7%A0%D7%A1-%D7%A2%D7%9D-%D7%A1%D7%95%D7%9C%D7%9C%D7%94-%D7%92%D7%93%D7%95%D7%9C%D7%94
http://www.mako.co.il/cars-road-tests/Article-36f2a0e81a57531006.htm
http://funginstitute.berkeley.edu/sites/default/files/The%20Electric%20Vehicle%20Battery%20Landscape%20-%20Opportunities%20and%20Challenges.pdf
Renault Fluence ZE
Tesla S
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.
Notes: YOU MIXED THEM UP I THINK!!!

## Slide 34
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 35: So where is the problem?...
13,080 NIS/yr subscription of 20,000 km(0.65 NIS/km)
Cost of “electric car km” is the equivalent of 0.65 NIS travel cost;
@ current fuel prices, a gasoline car consumes 11.8 km / liter.
Not worth to buy an electric car if there is no financial gain
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 36: So where is the problem?...
No financial gain using an electric car car from Better Place
The travel time is very short at full-charge.
Must always be prepared to search for a recharge station, not very many in the country.
Private parking is required
Battery technology is very expensive.
The battery does not provide a lot of energy
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 37
http://europa.eu/legislation_summaries/environment/air_pollution/l28186_en.htm
Environmental Accountability 2011- IEC
Chart: CO2 (kg)
| CO2
gasoline car | 3600
Renaoult | 5610
Tesla | 3570
Chart: particles (kg)
| particles
Gasoline car | 0.12
Renault | 0.462
Tesla | 0.294
Chart: NOx (kg)
| NOX
Gasoline car | 4.32
Renault | 16.5
Tesla | 10.5
Chart: CO (kg)
| CO
Gasoline car | 12
Renault | 44
Tesla | 16.5
Is Electricity Really Not Polluting?
http://www.carpages.co.uk/co2/
https://www.iec.co.il/environment/Documents/svivaty_iec_2011_hebrew.pdf
Possibility to monitor and manage the power plant’s pollutants is better than that for a lot of vehicles.
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.

## Slide 38: Is Electricity Really Not Polluting?
http://www.internationallawoffice.com/newsletters/detail.aspx?g=36990020-5a6a-4a82-9a15-35cfd96ac63c
If in the future it will be possible to generate electricity not from coal – but from renewables, then we will reduce the amount of pollution significantly.
© N. Baskin- Caesarea-Rothschild/ FGS Weizmann Inst.