## Slide 1
Resolving Cellular Specific Microarchitectures Using
Double Pulsed Field Gradient Weighted, Relaxation-Enhanced
Magnetic Resonance Spectroscopy
N. Shemesh1, J.T. Rosenberg2, J-N Dumez3, J.A. Muniz2,4, L. Frydman2,3 & S.C. Grant2,4
1 Champalimaud Neuroscience Programme, Champalimaud Centre for the Unknown, Lisbon, Portugal
2The National High Magnetic Field Laboratory Tallahassee FL, USA
3 Chemical Physics, Weizmann Institute of Science, Rehovot, Israel
4Chemical & Biochemical Engineering Florida State University, Tallahassee FL, USA
Nature Communications 2014 (5): 4958

## Slide 2
Speaker Name: Samuel C. Grant
I have no financial interests or relationships to disclose with regard to the subject matter of this presentation.
Declaration of Financial Interests or Relationships

## Slide 3: Stroke
Impacts on Public Health:
Leading cause of disability in the US
4th leading cause of mortality (1 of every 20 deaths)
  Annual cost > $73.3 billion
  Pathophysiology:
  Affected region depends on arterial blockage (ischemia) or rupture (hemorrhagic)
  Interruption of O2 & nutrients leads to a cascade of detrimental events:
    Na+/K+ ATPase unable to maintain ionic homeostasis
    Release of toxic excitatory amino acids and enzymes
    Necrosis at the core but extended impacts in penumbral tissue
    Osmolytes & metabolites can serve as probes/biomarkers for severity and outcome

## Slide 4
Diffusion MRS in Stroke
Restricted diffusion has central role in diagnosis & prognosis
Water-based diffusion weighted MRI is somewhat nonspecific
  Underlying diffusivity variations not understood
  Prevents probing of distinct cellular morphologies
Probing metabolic diffusion may tell another (better?) story
  Metabolites exhibit different, cell-specific compartmentalization
Eccentricity measurements by double Pulsed Field Gradients (dPFG) focusing on specific metabolites may provide unique information about cell-specific swelling with ischemia

## Slide 5
Selective excitation of metabolites
Overcomes many MRS limitations:
High SNR per unit time
Sensitivity via longitudinal relaxation enhancement (RE)
No J-modulations
No need to suppression the ~10,000x larger water peak
Red - Conventional water suppressed sequence
Blue – Selective excitation
Shemesh et al Chem Eur 2013
Novel approach to MRS

## Slide 6
Novel approach to RE-MRS
Clean and undistorted spectra used for T1 and T2 measurements at 21.1 T
Nature Comm. 2014. 5: 4958 & J Cereb Blood Flow Metab. 2014. 34(11): 1810.
Cre
Cho
NAA
Lac
SNRNAA = 29 ± 13 *
SNRLac = 25 ± 15 *
“H20”
SNRtCho = 19 ± 6 *
SNRtCre = 39 ± 11 *
Cre
Cho
NAA
Lac
SNRNAA = 58 ± 10
SNRLac = 9 ± 2
“H20”
SNRtCho = 29 ± 6
SNRtCre = 60 ± 12
Ipsilateral
Contralateral
b
TE (ms)
58
254
Cre
Cho
NAA
Lac
“H20”
T1
T2
Notes: Acquisition time!!

## Slide 7
Double Diffusion Encoded MRS
D-PFG principles:
  Pairs of diffusion sensitizing gradients G1 and G2 are applied and relative angle  is varied
First proposed by Cory (1990)
Employs 2nd diffusion gradient pair
Has a mixing time (tm)
Importantly, orientation of 2nd gradient is varied, not amplitude
Eccentricity measurements by dPFG
Notes: A double-PFG sequence. Note that two gradient pairs are applied in succession, with the timing between them defined as the mixing time (tm). In this specific sequence, the case of ψ = 180° is shown owing to the fourth and fifth 90° RF pulses. (G) The angular d-PFG methodology. Here, the gradient durations and amplitudes are set, along with the diffusion periods and the mixing time. What is varied is simply the relative angle between the gradient vectors, defined as ψ. Here, the experiment is shown in the X−Y

## Slide 8
Double Diffusion Encoded MRS
dPFG display modulation dependent on pore eccentricity
Evident even if compartments are randomly oriented
Angular DDE MRS could be used to infer
underlying microstructure
csA~0
csA
csA
csA
Özarslan, J. Magn. Reson. (2009)
At long tm , the E(ψ) plots reflect pore eccentricity (L/r)
Notes: A double-PFG sequence. Note that two gradient pairs are applied in succession, with the timing between them defined as the mixing time (tm). In this specific sequence, the case of ψ = 180° is shown owing to the fourth and fifth 90° RF pulses. (G) The angular d-PFG methodology. Here, the gradient durations and amplitudes are set, along with the diffusion periods and the mixing time. What is varied is simply the relative angle between the gradient vectors, defined as ψ. Here, the experiment is shown in the X−Y
csA - Compartmetn shape Anisotropy

## Slide 9: Metabolic DDE RE-MRS at 21.1 T
Objective:
Use selective excitation to probe in vivo microstructure and specific cell types through metabolic confinement

## Slide 10
DDE RE-MRS Method
Implementation at 21.1 T
dPFG module
G1 constant while varying G2 orientation to generate the relative angle 
Localized DDE MRS acquired in controls and 24 hr post stroke
Acquisition from (5-mm)3 voxel localized via a LASER module in ipsilateral (ischemic) & contralateral hemispheres

## Slide 11
Animal Model: Middle cerebral artery occlusion (MCAO)
(Longa et al. Stroke 1989; Uluç et al. J.Vis.Exp. 2011)
Animal work approved by FSU ACUC
Male Sprague Dawley rats ~250 g
Rubber coated filament through the external carotid artery (ECA)
1.5-hr occlusion following re-perfusion
Imaged 24-h post surgery
MR Equipment for in vivo Experiments:
21.1-T UWB magnet and PV 5.1
Gated during acquisition
NA=160 -> 4 min scan per angle
TR/TE=1500/187 ms
36 min total for nine  values / hemisphere
MRI & Animal Systems
User time available at:
www.nationalmaglab.org

## Slide 12
Quadrature Coil
70°
0°
60°
30°
15°
45°
90°
0°
60°
15°
45°
30°
75°
a
b
c
Sagittal
Axial
In vivo axial
15 mm
15 mm
15 mm
Homemade surface coil: designed and built at the Maglab
  Provided the sensitivity and B1 homogeneity over ROI
0.9 pF
0.9 pF
B1 flip map of a polyethylene glycol (PEG) and in vivo

## Slide 13
Results
Signal intensity from S0 and S() were fitted to:
S()/S0 = A+B(cos(2))
Amplitude modulation (B) was used to extract L/r ratios for each metabolite
Clean and undistorted peaks for easy fitting of each metabolite and hemisphere

## Slide 14
Results
L/r ratios reveal increase eccentricity
NAA, Cre & Cho show significant increase 24-h post MCAO
  (P<0.05, N=6 and one-way ANOVA with Fisher post hoc test)
Lac is diffusing in a less eccentric (more spherical) space after stroke compared to NAA
(P<0.05, N=6 and one-way ANOVA with Fisher post hoc test)
Metabolite | Contralateral | Ipsilateral
Lac | 9.7 ± 2.0 | 11.9 ± 0.9
NAA | 11.2 ± 0.9 | 12.7 ± 0.8*
Cre | 10.6 ± 0.9 | 12.5 ± 0.6*
Cho | 11.1 ± 0.8 | 12.1 ± 0.9*

## Slide 15
Cell-Specific Metabolic Confinement
DDE RE-MRS have been further modified to probe Neuronal (NAA) and Astrocytic (myoinositol) microstructure :
Both metabolites experience restricted diffusion
Show slightly different eccentricity ratios
 Demonstrates potential for reporting microstructural features from cell-specific MRS signals
Angewandte Chemie Int. Ed. 2015 In Review

## Slide 16
Conclusions
   4 min scan provides SNR (NAA) = 250 at =0
Selective excitation & RE provide high fidelity spectra & SNR needed for demanding dPFG studies
Long effective TE times predisposes DDE RE-MRS to long T2 species
However, metabolic T2s at 21.1 T are inherently long
Now able to probe metabolites confined to specific tissue
  NAA – neurons
  Myoinositol - astrocytes

## Slide 17: Acknowledgments
Technical Support
Fabian Calixto Bejarano
Jose Muniz
Funding provided by:
The American Heart Association
NSF (DMR-1157490)
The Florida State University
Visiting Scientist grant and UCGP from NHMFL

## Slide 18
Thank You!
User time available at:
www.nationalmaglab.org