## Slide 1: Observational techniques meeting #3

## Slide 2: Mirrors

## Slide 3: Classical mirrors: polished glass
Monolithic block of glass, polished to spec.
Largest good one is the 200” at Palomar (P200).
Limit is material strength of glass
Mirror surface is aluminized periodically

## Slide 4: Breakthroughs #1: honeycomb
Casting borosilicate glass (good thermally) onto a honeycomb ceramic mold in spinning oven
Structure allows lighter weight (20%), ventilation; spinning naturally sets parabolic form
Maximum size set by oven: 8.4m
Subaru, Magellan, MMT, LBT, GMT

## Slide 5: Breakthroughs #2: thin meniscus
Very thin mirror with active actuators to compensate for flexure in real time
Maximum size so far: 8.2m
NTT, Gemini, VLT, SOAR

## Slide 6: Breakthroughs #3: segmented
Replace large monolithic mirrors by actively-controlled (actuated) segments
Maximum size limited by support mechanics and computation, currently largest telescopes 10m
Keck, GTC, TMT, ELT

## Slide 7: Future prospect: liquid mirrors
Spinning liquid mirror naturally assumed parabolic form
Can be made from mercury
However: mercury is volatile, and poisonous
No current working models

## Slide 8: AO

## Slide 9: AO

## Slide 10: Celestial coordinates

## Slide 11: End