## Slide 1: Observational techniques meeting #6

## Slide 2: Topics for student talks:
Cosmic microwave background: history + basic instrumentation
CMB: recent developments
MM/SubMM instrumentation: SCUBA -> ALMA
Sunyaev-Zeldovich effect; detection; implications
Light echoes
IFU spectrographs
Polarization
Neutrino detectors
TeV telescopes
Cosmic-ray observatories
Gravitational wave detectors – LIGO
Future GW observatories - LISA
MIR/FIR instrumentation
X-ray astronomy (basic)
Advanced X-ray (Nustar; Athena)
X-ray polarimetry
JWST: the next generation space telescope
Astrometry and GAIA
Next generation cosmology missions: Euclid and WFIRST
Future radio arrays: LOFAR, SKA
UV observations
Robotics
Planetary missions

## Slide 3: Detectors

## Slide 4: CMOS (active pixel arrays)
Arrays of pixels, each composed on a photodetector (photodiode), amplifier, and readout electronics, realized on chip using CMOS technology
Material | Sensitivity range (nm)
Silicon | 190 - 1100
InGaAs | 800 - 2600
PbS | 1000 - 3500
High QE (>90%), fast readout, cheap, relatively high noise

## Slide 5: IR pixel arrays
Material | Sensitivity range (nm)
Silicon | 190 - 1100
Germanium | 500 - 1700
InGaAs | 800 - 2600
HgCdTe (MCT) | 800 - 10000
InSb | 1000 - 5500
NICMOS 3
He cooling
N cooling

## Slide 6: IR instruments: NICMOS
Instrument type | Camera and Spectrograph
Weight | 370 kg
Dimension | 2.2 m x 0.89 m x 0.89 m
Field of view | Low resolution 51.5” x 51.5” Medium resolution 17.5” x 17.5” High resolution 11.0” x 11.0”
Wavelength range | 800 to 2500 nm
Following servicing: move from cryo-cooling (He) to TE cooling (-77 C): unlimited lifetime, loss of K band (>1.7 micron)
MCT detector, 256 x 256 pixels

## Slide 7: IR instruments: WF3/IR
Components:
Teledyne 1Kx1K HgCdTe detector.
Total Field of View: 123 x 136“
Pixel Size: 0.13”
Nominal Operating Temperature: 145 K
Median Dark Current: 0.015 e-/sec/pix
Readnoise (CDS): 15.5 e-
Full Well: 93,000 e- (95% linearity)

## Slide 8: IR instruments: HAWK-I
New IR instrument on VLT (ESO). Cryogenic (120 K, detectors at 80 K) and has a full reflective design. The light passes four mirrors and two filter wheels before hitting a mosaic of four Hawaii 2RG 2048 * 2048 pixels detectors (Raytheon HgCdTe). The final
F-ratio is F/4.36

## Slide 9: IR instruments: VISTA
VISTA is a 4-m class wide field survey telescope for the southern hemisphere, equipped with a near infrared camera (1.65 degree diameter field of view at VISTA's nominal pixel size) containing 67 million pixels of mean size 0.34 arcsec and available broad band filters at Z,Y,J,H,Ks and a narrow band filter at 1.18 micron.
The telescope has an azimuth-altitude mount, and quasi-Ritchey-Chretien optics with a fast f/1 primary mirror giving an f/3.25 focus to the instrument at Cassegrain. The instrument mounts to the rotator on the back of the primary mirror cell, and includes a wide-field corrector lens system, autoguider and active optics sensors.
VISTA is located at ESO's Cerro Paranal Observatory in Chile
16 2048x2048 pixel IR detectors (Raytheon HgCdTe 0.84-2.5 micron)

## Slide 10: IR instruments: Spitzer
Spitzer is designed to detect infrared radiation. The Cryogenic Telescope Assembly, which contains a 85 cm telescope and Spitzer's three scientific instruments, is cooled to a few K with liquid helium (f/12 lightweight Beryllium mirror, cooled to less 5.5 K).
IRAC is a four-channel camera that provides simultaneous 5.12 x 5.12 arcmin images at 3.6, 4.5, 5.8, and 8 microns. The pixel size is 1.2 arcsec in all bands. All four detector arrays in the camera are 256 x 256 pixels in size, with the two short wavelength channels using InSb and the two longer wavelength channels using Si:As detectors.
The Multiband Imaging Photometer is an imaging camera in the far-infrared (24, 70 and 160 microns). MIPS is also capable of simple spectroscopy. At 24 micron mode 128 x 128 pixels; at 70 and 160 micron arrays are much smaller 32 x 32 and 2 x 20 pixels GeGa.. 5’ x 5’ section of the sky at any one time at 24 microns (less at 160)

## Slide 11: IR instruments: Herschel
ESA: FIR-submm 55 to 672 µm
Telescope - Cassegrain, 3.5m primary and 0.3m secondary mirror
HIFI: high resolution heterodynes spectrometer 157-625 µm
PACS, SPIRE: bolometer arrays

## Slide 12: IR instruments: JWST
6.5 space telescope
MIRI: The Mid-Infrared Instrument (MIRI) is an imager/spectrograph that covers the wavelength range of 5 to 27 micron with Si:As detector arrays. The nominal operating temperature is 7K.
The Near Infrared Camera (NIRCam), is an imager with a large field of view and high angular resolution, 0.6 - 5 micron with ten mercury-cadmium-telluride (HgCdTe) detector arrays.
NIRSpec: simultaneous spectra of more than 100 objects in a 9’ square field of view. Medium-resolution spectroscopy at 1 to 5 micron and lower-resolution spectroscopy from 0.6 to 5 micron. Two HgCdTe detector arrays.

## Slide 13: CMOS: fast cameras
Model | Active Pixels | Frame Rate | Dark Current
Neo 5.5 sCMOS | 2560 x 2160 | 30 | 0.007
Zyla 5.5 sCMOS | 2560 x 2160 | 100 (40 USB 3.0) | 0.14
Zyla 4.2 sCMOS | 2048 x 2048 | 100 (53 USB 3.0) | 0.14

## Slide 14: CMOS: fast cameras Application: KBOs
Schlichting, Ofek et al. 2009, Nature

## Slide 15: End